## Slide 1
Community Microgrid Initiative
Craig Lewis
Executive Director
650-796-2353 mobile
craig@clean-coalition.org
6 March 2025

## Slide 2: Types of microgrids
A microgrid is a combination of energy resources, definitely including generation, that are coordinated to serve specified loads, including in an islanded fashion.
A Solar Microgrid is a behind-the-meter (BTM) microgrid that solely relies on solar for energy generation when islanded. A Solar Microgrid relies on energy storage to time-shift solar and ensure energy availability at night etc.
A Hybrid Solar Microgrid is a Solar Microgrid that includes additional sources of energy generation, beyond just solar.
A Community Microgrid a microgrid that covers a target grid area and relies on existing distribution feeders (ie, power lines) to operate when islanded. Community Microgrids typically include both front-of-meter (FOM) and BTM resources, including Solar Microgrids, and require effective participation from utilities, which have mostly erected barriers to date.

## Slide 3: Community Microgrids within Distribution grids
High-Voltage
Transmission
grid
Low-Voltage
Transmission
grid
Distribution grid
Notes: Market distortions like the erroneous metering & assessment of Transmission Access Charges (TAC) for California IOUs creates massive market distortions that steal value from local generation, hurt ratepayers, and preempt energy resilience.
Non-PTO utilities (metered sub-systems) currently operate under the system we are proposing. The Clean Coalition TAC fix would bring consistent TAC treatment to DG resources in all utility service territories.

## Slide 4: Transmission & Distribution grids are different
70 KV
70 KV

## Slide 5: Goleta Load Pocket (GLP)
The GLP is the perfect opportunity for a comprehensive Community Microgrid
GLP spans 70 miles of California coastline, from Point Conception to Lake Casitas, encompassing the cities of Goleta, Santa Barbara (including Montecito), and Carpinteria.
GLP is highly transmission-vulnerable and disaster-prone (fire, landslide, earthquake).
200 megawatts (MW) of solar and 400 megawatt-hours (MWh) of energy storage will provide 100% protection to GLP against a complete transmission outage (“N-2 event”).
  200 MW of solar is equivalent to about 5 times the amount of solar currently deployed in the GLP and represents about 25% of the energy mix.
  Multi-GWs of solar siting opportunity exists on commercial-scale built-environments like parking lots, parking structures, and rooftops; and 200 MW represents about 7% of the technical siting potential.
  Other resources like energy efficiency, demand response, and offshore wind can significantly reduce solar+storage requirements.

## Slide 6: Core load area of the GLP
Legend
16kV Gladiola Feeder
Substations
16kV Gaucho Feeder
16kV Professor Feeder
UCSB
Santa Barbara Airport
Tier 3 Fire Threat
Tier 2 Fire Threat
220 kV Transmission
Feeder #4157
Feeder #3556
Feeder #3559
Feeder #4169
Feeder #3565
Feeder #4227
Feeder #4311

## Slide 7: Target 66kV feeder serves critical GLP loads
Legend
16kV Gladiola Feeder
Substations
16kV Gaucho Feeder
16kV Professor Feeder
Dos Pueblos High School
Santa Barbara Airport
Tier 3 Fire Threat
66 kV Feeder #4311
Fire Stations
Goleta Sanitary District
Planned Battery Energy Storage
Goleta Valley Cottage Hospital
Direct Relief
Fire Station # 17
Direct Relief (Solar Microgrid)
Vegas Substation
Isla Vista Substation
Goleta Energy Storage Project
(240 MWh)
Fire Station # 8
Goleta Sanitary District
Deckers
UCSB
SB Airport
Bella Battery Energy Storage Project (120 MWh)
Dos Pueblos High School (Solar Microgrid)
University of California Santa Barbara
Ellwood Gas Peaker Plant

## Slide 8: GLP Community Microgrid – first big chunk
Isla Vista Substation (66-to-16kV)
Fire Station #17
66kV underground interconnection
Vegas Substation (66-to-16kV)
UCSB
+ Solar
SBA (runway lights & ATC)
Direct Relief
+ Solar Microgrid
SBA (Main Terminal)
Goleta Sanitary District
Goleta Substation (220-to-66kV)
Diagram Elements
66 kV Distribution Feeder #4311
16 kV Gladiola Feeder
16 kV Gaucho Feeder
16 kV Professor Feeder
16 kV Los Carneros Feeder
16 kV Ace Feeder
16 kV Storke Feeder
Planned Battery Energy Storage
Ellwood Gas Peaker Plant
Grid isolation switch (open, closed)
Smart meter switch (open, closed)
Fire Station #8
66kV distribution feeder #4311 with multiple branches
Deckers
+ Solar
Tier 2 & 3 facilities
Tier 2 & 3 facilities
GridStor BESS
(240 MWh)
Goleta Substation has eight feeders, seven 66 kV & one 16 kV, that serve the entire GLP
Tier 2 & 3 facilities
Greenbark BESS
(120 MWh)
Ellwood Gas Peaker Plant
Karl Storz + Solar Microgrid
Costco
+ Solar
Dos Pueblos
+ Solar Microgrid
San Marcos
+ Solar Microgrid
Goleta Cottage Hospital
City of Goleta
+ Solar

## Slide 9: Community Microgrid Initiative
The Clean Coalition established the Community Microgrid Initiative in 2010 to harness local solar and energy storage to deliver an unparalleled trifecta of economic, environmental, and resilience benefits to communities.
https://clean-coalition.org/community-microgrid-initiative/
Notes: 9

## Slide 10: Long history of Community Microgrids
  Hunters Point Community Microgrid (San Francisco, CA)
  Long Island Community Microgrid (East Hampton, NY)
  Valencia Gardens Energy Storage (San Francisco, CA)
  Redwood Coast Airport Microgrid (Humboldt County, CA)
  Montecito Community Microgrid (Montecito, CA)
  Goleta Load Pocket Community Microgrid (Santa Barbara County, CA)
  Berkeley Efficient Mixed-Use Showcase (Berkeley, CA)
  Orcas Community Microgrid (San Jaun Islands, WA)
  Sierra Blanca Community Microgrid (La Quinta, CA)
  Tomales West Community Microgrid (Marin County, CA)
  East LA Community Microgrid (Los Angeles County, CA)
  Kapalama Container Terminal Community Microgrid (Honolulu, HI)

## Slide 11: Community Microgrid stakeholders
Community Microgrid
Financiers
Solution Providers
Utilities
Property Owners
Municipalities
Residents
Philanthropic
Funders
Policymakers

## Slide 12: Value-of-Resilience methodology
VOR123
VOR123 is the value-of-resilience (VOR) from Solar Microgrids methodology that the Clean Coalition has developed to normalize VOR across all types of facilities & geographies. The VOR normalization is founded in tiering loads into three categories: Tier 1 (critical), Tier 2 (priority), and Tier 3 (discretionary). Since each Tier has its own resilience requirement and VOR, this methodology is called VOR123.
VOR123 webinar
https://clean-coalition.org/news/webinar-valuing-resilience-solar-microgrids-thursday-5-nov-2020/
Notes: 12

## Slide 13: Resilient Energy Subscription
Resilient Energy Subscription is a market mechanism designed to ensure that facilities can subscribe to guaranteed levels of daily energy generation while the associated fees maximize Community Microgrid proliferation.
https://clean-coalition.org/resilient-energy-subscription-res/
Notes:   Community Microgrids have the same solar+storage ratios as individual Solar Microgrids.
  Facilities in a grid area can be tiered in a similar manner to loads, based on how critical a facility is to a community.
  For Critical Community Facilities (CCFs), the Community Microgrid costs should be rate-based, on a cost-of-service basis, just like the cost of every other grid asset that serves the community at large.

## Slide 14: Community Microgrid examples in focus
Community Microgrid examples in focus

## Slide 15: PG&E MIP Tranche 1 Master Scorecard Results

## Slide 16: Tomales West Community Microgrid (TWCM) project area
Fire Station
Tier 2 High Fire Threat
Cotati 12kV feeder
Grid Isolation Switch
Presbyterian Church
(Sheltering Center)
Church of the Assumption
(Sheltering Center)
Wastewater Lift Station
Undergrounding
Existing Feeder
(250 feet)
297 kWdc solar & 326 kW / 1,306 kWh BESS
SUSD Bus Parking and Surplus Facilities
(Solar & BESS Siting)

## Slide 17: 534 kW solar siting potential on SUSD parcels (only need 300 kW to satisfy MIP resilience requirement)
Ground Mount 135 kW
Solar Canopies (2x) 124 kW total
Solar Canopy 83 kW
Solar Canopy 109 kW
Solar Canopy 83 kW

## Slide 18: Tomales West Community Microgrid diagram
Cotati 12kV along 1st Street
Residential Customers
Residential Customers
Fire Station
BESS
326 kW
1,306 kWh
Solar
297kW
Sheltering Station
Sheltering Station
Cotati 12kV continues
Wastewater Lift Station
Cotati 12kV along
Tomales-Petaluma Rd
Cotati 12kV continues
LR3
LR2
LR4
LR148
PG&E Distribution Control Center
Microgrid Controller
Existing infrastructure, included in CMG
PG&E Resources
Existing Sites
New infrastructure, CMG, undergrounded
Legend
New Resources
Existing infrastructure, outside of CMG
Existing infrastructure to be undergrounded
Communications
Primary Point of Interconnection
Grounding Transformer
Preliminary design pending PG&E approval
Notes: 18

## Slide 19: Point Reyes Station West
Tier 2 High Fire Threat
Olema 12kV feeder
Grid Isolation Switch
Health & Human Services and Clinic
Low-Income Senior Housing
Fire Station & Sheriff Office
Dance Palace Community Center
737 kWdc solar & 1,467 kW / 5,875 kWh BESS

## Slide 20: Point Reyes Station East
Tier 2 High Fire Threat
Olema 12kV feeder
Grid Isolation Switch
Elementary School
Food Pantry & Radio Station
246 kWdc solar & 489kW / 1,958 kWh BESS
Presbyterian Church

## Slide 21: Tomales East critical community facilities and distances within Tier 2 Fire Threat for potential undergrounding
High School
Wastewater System
New Feeder
0.25 miles
School District Office
Elementary School
Tier 2 High Fire Threat
Cotati 12kV feeder
Grid Isolation Switch
Existing Feeder
0.79 miles
Existing Feeder
0.27 miles
1,144 kWdc solar & 964 kW / 1,927 kWh BESS

## Slide 22: Marshall critical community facilities and distances within Tier 2 Fire Threat for potential undergrounding
Tier 2 High Fire Threat
Olema 12kV feeder
Grid Isolation Switch
Wastewater System
Marconi Conference Center
(Sheltering)
Existing Feeder
0.4 miles
1,500 kWdc solar & 653 kW / 2,611 kWh BESS

## Slide 23: East LA Community Microgrid layout
Transformer
#5147414
BESS 1 & Resource Controller Location Option #2
Transformer
#5482396
BESS 1 & Resource Controller Location Option #1
“Solar 5”
502 kW Solar Parking Garage Canopy
“Solar 4”
598 kW Solar Parking Canopies
“Solar 1”
357 kW Rooftop Solar
“Solar 2”
54 kW Rooftop Solar
“Solar 3”
137 kW Rooftop Solar
MIP application pending final SCE approval

## Slide 24: KCT Community Microgrid
KCT Community Microgrid
Kapalama Container Terminal is fully electrified and under construction in Honolulu, HI.

## Slide 25: KCT Community Microgrid diagram
BESS
EVCI
4
2
3
1
PV
Comfort Station
Admin & Maintenance Bldgs
Guard Shack
Marine Ops Bldg
Grid
Isolation
Switch
6
5
7
8
Reefer Loads*
10
BESS
Cranes
Yard
Lighting
BESS
EVCI
PV
Reefer Loads*
Reefer Loads*
Reefer Loads*
PV
BESS
PV
BESS
PV
BESS
PV
BESS
Reefer canopies not committed
9
HECO “Macrogrid”
“Hybrid Microgrid” application pending HECO approval
Auiki
Substation
Notes: The reefers are not part of the microgrid.
Feeder operates like a normal feeder when the Grid Isolation Switch (GIS) is closed.
When the GIS is open, everything to its left becomes self-sustaining (ie, islanded).

## Slide 26: KCT site overview (7MW solar siting potential)
Auiki Substation
R-1
Admin building (58 kWdc)
Pasha Kapalama Container Terminal
19 Sand Island Access Rd, Honolulu
Full Site Overview
SUB
Potential EVSE (<20 kW, 150+ kW)
Total Solar Siting Potential: 7,000 kWdc
R-2
Maintenance building (398 kWdc)
R-3
Marine Ops rooftop (15 kWdc)
C-1
Admin parking canopy (482 kWdc)
C-3
C-1
C-3
R-1
R-2
R-3
SUB
C-4
Marine Ops parking canopies (430 kWdc)
C-3
Meter locations
N
Marine Ops north canopy (122 kWdc)
14,453 kW / 28,905 kWh BESS
C-2
C-2
C-2
Reefer canopies x8 (5,491 kWdc)
Baseline Load Profile: 48,409,206 kWh
Adjustment Load Profile: 1,497,393 kWh
Master Load Profile: 49,906,599 kWh
Annual Solar Generation: 12,488,963 kWh